## Slide 1
Fernando Tornos, Lluis Boixet, Maria Zaparain, Luis Perez & Fidel Ribera
The Zn-Pb-rich belt of NW Iberia.
A syn-tectonic stratabound mineralization?
Notes: A lo largo de los más de 30 años de actividad investigadora he seguido una línea de investigación uniforme con un motivo central y único: EL ESTUDIO DE LAS ROCAS GRANÍTICAS con un fin esencial: CONOCER LOS PROCESOS DE GENERACIÓN Y RECICLAJE DE CORTEZA CONTINENTAL

## Slide 2: The Zn-Pb Belt
Discovered 1967
Mined out 1977-1991 (EXMINESA)
18.6 Mt @ 17.3%Zn & 1.3%Pb
Historical mine
1965-1972 (Rio Kumer)
Evaluated 1972-1978 SMMPE
4.74 Mt @ 5.5% Zn & 4.39%Pb
Discovered 1975
Unmined
Evaluated 1975-1980 (SMMPE), 1980-1985 (ENADIMSA), 2018- (Europa Metals)
20 Mt @ 4.4%Zn, 2.8%Pb & 23 g/t Ag
Zn
Zn+Pb

## Slide 3: Stratabound control

## Slide 4: Stratigraphic section and mineralization
Early Cambrian regionally extensive limestone unit
Regionally extensive (barren) dolomitization
Discontinuous Zn-Pb Belt in SW Europe
  Sardinia & Massif central
Four types of mineralization
  (A) Stratiform mineralization in V1 (+barite)
  (B) Silica-rich ore in V3
  (C) Carbonate-chlorite ore in V3
  (D) Shear-zone controlled in V1
Fe-poor Hg-bearing sphalerite – galena
Pyrite, chalcopyrite, As-Co-Ni sulfides, tetrahedrite, bismuthinite, Pb-Bi-Ag sulfosalts
Los Cabos Fm (>1,000 m; CA2-O1)
Candana Fm (≈1,600m; CA1)
Vegadeo Fm (CA1-2)
V2
V1
V3
A
D
B
C
Carbonate-chlorite Ore
Silica Ore

## Slide 5: The protore: early diagenetic stratiform mineralization?
Abundant low grade stratiform mineralization in V1
Hosted by unaltered oolitic bars
Most likely protore: do high grade deposits represent their hydrothermal remobilization?

## Slide 6: Shear zone-related mineralization (V1)
Rubiales mine (+ Mercurin)
Ore controlled by D3 vertical shear zones
  Massive ore replacing silicified limestone
    External halo of ankerite
  Veins and breccias in shale with phyllic alteration
Significant enrichment in py-po / late chloritization
Rubiales

## Slide 7: Stratabound mineralization: silica ore (V3)
Contact V3 - shale
Tens of small prospects variable grade & tonnage
Regionally extensive multistage silicification (>40 km)
Small front of mineralized polymictic breccia supported by dolostone
do
shale

## Slide 8: Stratabound mineralization: carbonate-chlorite ore (V3)
In the southern part: Toral and Antonina projects
Lateral to silica ore: Sharp contact (?)
Replacing limestone and stockwork/veins in external halo
Chlorite ± clays ± calcite supporting carbonate-(shale) breccia: crackle to heterogeneous
Dissolution of limestone accompanied by precipitation of phyllosilicates and sulfides
Silica ore
Breccia

## Slide 9: Origin of metals and fluids: lead isotopes
Chart: 206Pb/204Pb
| 17.832599999999999 | 17.8279 | 17.801300000000001 | 17.823699999999999 | 17.835000000000001 | 17.836200000000002 | 17.900500000000001 | 17.853400000000001
HW Vegadeo | 15.6079 | 15.6048 | 15.5816 | 15.587 | 15.5986 | 15.5981 | 15.6405 | 15.5854
Rubiales | 15.607 | 15.629 | 15.63 | 15.593 | 15.614 | 15.602 | 15.59
 | 15.629 | 15.627 | 15.624 | 15.622 | 15.618 | 15.617 | 15.615 | 15.613 | 15.611 | 15.61 | 15.61 | 15.606 | 15.599 | 15.594 | 15.591 | 15.586 | 15.583 | 15.576 | 15.572 | 15.565 | 15.559
 | 15.678 | 15.676 | 15.673 | 15.671 | 15.667 | 15.666 | 15.664 | 15.662 | 15.66 | 15.66 | 15.659 | 15.655 | 15.648 | 15.644 | 15.641 | 15.636 | 15.633 | 15.626 | 15.622 | 15.616 | 15.609
 | 12.12 | 13.44 | 14.25 | 14.78 | 15.13 | 15.37 | 15.52 | 15.6 | 15.66 | 15.69 | 15.7

## Slide 10: Sulfur isotopes
Seawater sulfate
d34S ≈+27 to +30‰
Stratiform mineralization (V1)
d34S +28.2 to +35.0‰
Stratabound mineralization (V3)
d34S +18.2 to +25.3‰
Diagenetic pyrite in shale
d34S +9.8 to +15.9‰
Shear zone-related mineralization (V1)
d34S +25.6 ±0.5 (sph) 22.5±0.5 (gn)
(Fast) biogenic reduction in a system poor in organic matter
minimal fractionation
Mixing from two sources (ca 50%?)
Algal/microbial mats
Ghosts of evaporites

## Slide 11: A bit more of geochemistry…
d18O-dD values suggest fluids equilibrated with siliciclastic rocks
d18Ofluid: +4.8 to +6.1; dD: -53 to -48‰
Basinal/low grade metamorphic fluids
87Sr/86Sr > 0.7149: not equilibrated with carbonates (≈ 0.7098) - more radiogenic shale or basement
Fluids temperature 150-200°C; aqueous low salinity (<7 wt%)?
These fluids are different than those related to regional dolomitization

## Slide 12: Timing of the mineralization
Variscan Deformation: 360-340 Ma (D1-D2)  315-304 Ma (D3)
Breccias includes fragments of shale
  Postdate deposition (and cleavage) of shale
Rubiales: 307±7 Ma (K-Ar)
Silica Ore: 323±7 & 320±6 Ma (K-Ar)
Paleomagnetism: post-folding event (Ruiz et al. submitted)
Main mineralization is late Variscan in age: coeval with D3 shearing
  Protore (stratiform mineralization) probably early Cambrian

## Slide 13: Genetic models
Few equivalents: dissimilar MVT, Irish Type and sediment hosted
“Siliceous Crust Type”? (Brigo et al. 2001)
  Early diagenetic
“Syn-sedimentary”
  Related to karst + paleosoils in vadose setting (Rabu, 1977; Hermosa, 1995)
  Sedimentary exhalative (Luque, 1985)
Stratiform mineralization: Early diagenetic (equivalent to others in SW Variscan Belt)
Rubiales: shear-zone controlled (Luque & Ruiz, 1990; Arias et al. 1991)
Stratabound: Late Variscan replacement
Different to other carbonate-hosted deposits of the Variscan Belt

## Slide 14: Some numbers…
Tornos & Heinrich (2008)
9 wt% NaCl eq.
L-V
Fluids can transport large amounts of Zn-Pb (but low H2S) between ca. 240-310°C
Reaction with limestone produces silicification but small mineralization
Cooling does not work, either
Need an extra source of reduced sulfur: fluid mixing!

## Slide 15: Fluid mixing along paleoaquifers is the key
Ascent of fluids along shear zones during D3
Partial dissolution of the stratiform mineralization (protore)
Fluid circulation along a paleoaquifer controlled by the carbonate-shale contact
Reaction with limestone + fluid mixing with stagnant fluid rich in H2S
Breccias?
  Metasomatic front?
  Consistent with metal zonation

## Slide 16: Implications for exploration
Underexplored area
Syn-Variscan mineral system
  Large proportion of potential hosts in the area
  Large volumes of potential sources for fluids and metals
  Channelways for hot fluids
Two major traps
  Shear zones when crosscutting carbonatic rocks
  Contacts between shale and carbonatic rocks
Broadly equivalent to MVT/Irish deposits but in internal parts of orogens
  Higher temperature allows silica precipitation
  Wonder, why not more?

## Slide 17: Thanks to…
And IAEG for the invitation!!
f.tornos@csic.es
Thanks to:
Carmen Galindo & J.M. Fuenlabrada (UCM)
Tom J. Shepherd & Baruch Spiro
Jose Luis Hermosa
Carlos Ruiz (UCM)